## Slide 1
⚡ ENTERPRISE EDA CAD WORKBENCH
An Explainable AI-Assisted Early Timing Violation Prediction and Optimization Framework Using Open-Source EDA Tools
• Domain: VLSI Physical Design Automation & Explainable AI (XAI)
• Target PDK: Nangate 45nm Standard Cell Open Library
• EDA Integration: Yosys 0.38 (Synthesis) | OpenROAD 2.0 (Layout) | OpenSTA 2.5 (Timing)

## Slide 2
VLSI CAD & AI FRAMEWORK
Proposed Work & Key Objectives
📌 Problem Statement
• Traditional ASIC physical design sign-off requires hours of full routing and Static Timing Analysis (STA) iterations.
• Detecting setup timing violations (WNS < 0) late in the flow causes major Turnaround Time (TAT) delays.
• Fixing timing failures late requires costly re-synthesis and re-routing loops.
🎯 Proposed Solution
• Early Prediction: Predict setup violations post-placement PRIOR to detailed routing using Random Forest & XGBoost (97.29% accuracy).
• Open-Source EDA Tool Chain: Seamless integration of Yosys, OpenROAD, and OpenSTA.
• Explainable AI (SHAP): Identifies logic depth, fanout, and congestion as failure drivers.
• Automated Directives: Recommends pipeline register insertion, buffering, and cell upsizing.
• Interactive CAD Workbench: Provides Streamlit web UI and IEEE PDF report exporter.

## Slide 3
VLSI CAD & AI FRAMEWORK
System Architecture & CAD Pipeline
1. Input RTL
Verilog Source (.v/.sv) Syntax Checker Visual Schematic
2. EDA Flow
Yosys Synthesis OpenROAD Placement OpenSTA Timing
3. ML Engine
16D Feature Extractor Standard Scaler Random Forest / XGB
4. Closure
SHAP Feature Driver Optimization Directives PDF Sign-Off Report

## Slide 4
VLSI CAD & AI FRAMEWORK
Hardware & Software Requirements
💻 Software Specifications
• Operating System: Windows 10/11 / Linux Ubuntu 22.04
• Synthesis Engine: Yosys 0.38 Open-Source Tool
• Physical Layout: OpenROAD 2.0 (Place, CTS, Route)
• Timing Engine: OpenSTA 2.5 Static Timing Analyzer
• Target PDK: Nangate 45nm Open Cell Library
• Machine Learning: Python 3.13, Scikit-Learn 1.6, XGBoost 2.1
• Explainable AI: SHAP 0.46 Feature Attribution Engine
• CAD Interface: Streamlit 1.39 Enterprise Framework
🖥️ Hardware Specifications
• Processor: Intel Core i5/i7/i9 or AMD Ryzen 5/7/9 (Multi-Core 3.0 GHz+)
• System Memory (RAM): Minimum 8 GB (16 GB Recommended)
• Storage Space: 5 GB available SSD storage space
• Execution Mode: Cross-Platform Native Binary & Calibrated PDK Prototype Engine

## Slide 5
VLSI CAD & AI FRAMEWORK
Technical Methodology
⚙️ 7-Stage Timing Closure Execution Pipeline
1. RTL Ingestion & Syntax Check: Verilog port balancing, module validation, and Graphviz schematic rendering.
2. Yosys Gate Synthesis: Gate-level mapping to Nangate 45nm technology library.
3. OpenROAD Layout Extraction: Floorplanning, placement density, CTS, and net wirelength calculation.
4. OpenSTA Timing Analysis: Setup slack (WNS/TNS) and critical path delay extraction.
5. 16D Feature Extraction: Microarchitectural & physical layout vector formulation.
6. ML Classification & SHAP Drivers: Random Forest/XGBoost prediction (97.29% accuracy) & failure driver ranking.
7. Automated Optimization Directives: Pipelining register insertion, cell resizing, and IEEE PDF report export.

## Slide 6
VLSI CAD & AI FRAMEWORK
Experimental Results & Validation Metrics
Dataset Metric | Value
Total Valid Design Sweeps | 1,105
Timing Violation Samples (WNS < 0) | 561
Non-Violation Samples (WNS >= 0) | 544
Train / Test Split | 884 / 221 (80/20)
Model Metric | Score (%)
Random Forest Accuracy | 97.29%
Precision Score | 99.07%
Recall Score | 95.54%
F1-Score | 97.27%
Design Variant | Logic Depth | Critical Path | OpenSTA Status | ML Prediction
Unoptimized Multiplier (multiplier_unoptimized) | 18 levels | 1.85 ns | Violation (WNS = -0.85ns) | VIOLATION (94.2%) ❌
Optimized Multiplier (multiplier_optimized) | 7 levels | 0.78 ns | Pass (WNS = +0.22ns) | PASSED (95.9%) ✅

## Slide 7
VLSI CAD & AI FRAMEWORK
Conclusion & Key Contributions
🏁 Summary of Project Contributions
• High Predictive Accuracy (97.29%): Accurately predicts setup timing violations post-placement before time-consuming routing sign-off.
• Explainable Machine Learning: Uses SHAP attribution to rank logic depth and routing congestion as primary failure causes.
• Proven Timing Closure: Demonstrated timing violation removal by transforming an unpipelined multiplier (WNS = -0.85ns) into a 2-stage pipelined multiplier (WNS = +0.22ns).
• Fully Integrated Open-Source Toolchain: Seamlessly connects Yosys, OpenROAD, OpenSTA, Streamlit CAD dashboard, and IEEE PDF report generation.